EX-1700  FIELD PROGRAMMING SOFTWARE  
              For the IC-M10A and IC-M10E

Copyright 1991-1994 Icom Inc.
Portions of this software are copyrighted by Microsoft Corporation 1982-1988

     **                                                       **
     **  This program is designed to perform cloning for the  **
     **  IC-M10A/E VHF MARINE TRANSCEIVER only.               **
     **  Before using the program, make a backup copy of the  **
     **  original disk.                                       **
     **                                                       **



-------------------------------------------------------------------------------
TABLE OF CONTENTS 
-------------------------------------------------------------------------------


      1.  PROGRAM START UP AND SHUT DOWN ...................  2


      2.  OPERATION ........................................  2


      3.  SCREEN DESCRIPTIONS ..............................  3

            COMMON SCREEN ..................................  3
            MEMORY CHANNEL SCREEN ..........................  7
            INT CHANNEL and USA CHANNEL SCREENS ............ 10
            PRIVATE CHANNEL SCREENS ........................ 12
            FREE CHANNEL SCREEN ............................ 14
            WX CHANNEL SCREEN .............................. 16


      4.  CLONING OPERATION ................................ 17


      5.  FILE SAVING AND LOADING .......................... 19


      6.  PRINTING ......................................... 21


















                                    - 1 -



-------------------------------------------------------------------------------
1. PROGRAM START UP AND SHUT DOWN
-------------------------------------------------------------------------------

1) Boot up DOS.
2) Insert the EX-1700 backup disk.
3) Type the start command:

         **                                      **
         **  EX1700 /(version) / expert [Enter]  **
         **                                      **

     1. USA, UK, EUR, HOL, or FRA can be used as "(version)".
     2. When the version is specified, the corresponding
        default settings are read.
     3. When no version is specified, the previously
        saved contents are called.
     4. When "expert" is specified, additional items appear in the COMMON
        screen.
     5. When a file name is used instead of "(/version)," the specified file
        is loaded at startup.

4) The COMMON screen appears. 
       **                                                              **
       **  The loaded file name appears in the bottom left corner of   **
       **  the screen.  "NONAME.ICF" appears when no data file is      **
       **  loaded.                                                     **
       **                                                              **

5) When programming is completed:
   push [Esc] (indicates the TOP menu)
     then [F] (selects file SUB menu)
     then [S] (saves the set data; if not necessary skip this operation.)  
     then [Q] (quits the program)



-------------------------------------------------------------------------------
2. OPERATION
-------------------------------------------------------------------------------

The EX-1700 has a TOP menu and 8 screens for programming.  All screens or
operations can be accessed from the TOP menu. A SUB menu appears under the TOP
menu when the item in the top menu is selected with the [Arrow] and [Enter]
keys.  The TOP menu appears when the [Esc] key is pushed.

1) After the program starts up, push the [Esc] key to indicate the top menu.

2) Push a highlighted character; or the [Arrow] and [Enter] keys to select
   the desired item.
    - A SUB menu appears under the selected item.

3) Push a highlighted character; or the [Arrow] key and [Enter] keys to
   select the desired screen.
    - The desired screen appears.

4) Select the desired item with an [Arrow] key, then push [Space] or the 
   digit keys to set the item.
     - See descriptions of each screen for details.



                                    - 2 -



-------------------------------------------------------------------------------
3. SCREEN DESCRIPTIONS
-------------------------------------------------------------------------------

////// COMMON SCREEN //////

+[COMMON]---------+------------++-----------------+-----------+
| TITLE           |            || TITLE           |           |
+-----------------+------------++-----------------+-----------+
| ATIS ID         |        OFF || TX without ATIS |  INHIBIT  |
| ATIS INTERVAL   |        299 || --------------- | --------- |
| T.O.T. (Sec)    |        OFF || USA ch          |  ENABLE   |
| POWER SAVE      |        1/4 || WX  ch          |  ENABLE   |
| SCRAMBLER CODE  |          0 || S.CODE SEARCH   |  DISABLE  |
| SQL. LEVEL      |          0 || SCAN MENU       |  APPEAR   |
| SCAN MODE       |  NORMAL    || SCAN FUNCTION   |  ENABLE   |
| DUAL / TRI MODE |  TRI-WATCH || WATCH MENU      |  APPEAR   |
+-----------------+------------++-----------------+-----------+
  
                               **                                        **
                               ** NOTE: The items on the right side of   **
                               **       the screen only appear when      **
                               **       "expert" is specified during     **
                               **       program startup (p. 2 ).         **
                               **                                        **


SCREEN SELECTION

1) Push [Esc] key once or twice to indicate the TOP menu.

2) Select "Screen" with the [S] key, or the [Arrow] and [Enter] keys.
    - A sub menu appears under the TOP menu.

3) Select "Common" with the [C] key, or the [Arrow] and [Enter] keys.
    - The COMMON screen appears.



ATIS ID
   Funtions for Holland and Germany versions only.  The authorized
   ATIS code of the transceiver can be programmed in this item. This
   programmed ATIS code is used for ATIS encode and decode.

     **                                                            **
     ** IMPORTANT:  If the wrong code is programmed in this item,  ** 
     **             your ATIS code will confuse other ships.       ** 
     **                                                            **

       Selectable value:     OFF or 0000000000 to 9999999999
                             (Only 10-digit numbers accepted.)

       Selection method:     Push the [Space] key to turn the item OFF or;
                             Push digit keys, then [Enter] for code entry.








�@�@�@�@�@�@�@�@�@�@�@�@�@�@�@�@�@�@- 3 -



ATIS INTERVAL
   Funtions for Holland and Germany versions only.  The ATIS code is transmitted
   not only at the end of a transmission but also at intervals while 
   transmitting for long periods.  The interval of the ATIS transmission can be
   set.

        Selectable value:    1 to 999 sec.

        Selection method:    Push digit keys, then [Enter] for time entry.



T.O.T.(Sec)
   The time-out-timer function inhibits long transmissions.  The timer 
   starts counting from the beginning of a transmission.

        Selectable value:    OFF or 1 to 999 sec.
       
        Selection method:    Push the [Space] key for OFF or;
                             Push digit keys, then [Enter] for time entry.




POWER SAVE
  This item sets the duty cycle for the transceiver's power save function.
  This setting can also be performed using the transceiver's SET mode.

       Selectable value:    1/4, 1/8  or OFF

       Selection method:    Push [Space] to toggle the selection.



SCRAMBLER CODE
   A scrambler unit (UT-98) can be used with the transceiver.  When
   communicating using the voice scrambler function, remember that all members
   of a group must use the same scramble code. This setting can also be
   performed using the transceiver's front panel.

        Selectable value:    0 to 127 

        Selection method:    Push digit keys, then [Enter] for code entry.



SQL. LEVEL
   The IC-M10A/E's squelch can be set through CPU control. There are 9
   squelch levels available, 0-8. "0" opens the squelch completely - all
   signals can be received; "8" closes the squelch tightly - only strong
   signals can be received. The squelch level can also be set using the
   transceiver's front panel.

        Selectable value:    0 to 8

        Selection method:    Push digit keys, then [Enter] for squelch level.

        




                                    - 4 -



SCAN MODE
   The transceiver has 2 scan modes: normal and priority. Normal scan searches
   all channels in sequence; priority scan monitors channel 16 while searching
   all channels in sequence. When the SCAN FUNCTION item (p. 6) is set to 
   DISABLE, this item is not available.

       Selectable value:     NORMAL or PRIORITY

       Selection method:    Push [Space] or [Backspace] to toggle the
                            selection.



DUAL / TRI MODE
   The transceiver's watch function can be set to monitor channel 16 and a 
   selected channel - DUALWATCH; or, it can be set to monitor channel 16, the
   call channel and a selected channel - TRI-WATCH.

        Selectable value:    DUALWATCH or TRI-WATCH

        Selection method:    Push [Space] or [Backspace] to toggle the
                             selection.



The following items in the COMMON screen are only available when specifying
"expert" during program startup.



TX without ATIS
   Functions for Holland and Germany versions only.  A transmission can be 
   inhibited when no ATIS code is programmed.  If this setting is set to 
   "INHIBIT" without ATIS programming, the  transceiver can receive only.

        Selectable value:    ACCEPT or INHIBIT

        Selection method:    Push [Space] or [Backspace] to toggle the
                             selection.



USA ch
   U.S.A. channels can enabled or disabled using this item.

        Selectable value:    ENABLE or DISABLE

        Selection method:    Push [Space] or [Backspace] to toggle the
                             selection. 



WX  ch
   Weather channels can be enabled or disabled using this item.

        Selectable value:    ENABLE or DISABLE

        Selection method:    Push [Space] or [Backspace] to toggle the 
                             selection.



                                    - 5 -



S.CODE SEARCH
   This item allows a user to determine the scramble code for a received
   signal when it is not known in advance.

        Selectable value:    ENABLE or DISABLE

        Selection method:    Push [Space] or [Backspace] to toggle the
                             selection.



SCAN MENU
   This item is used to add or remove scan type selection (normal or priority)
   from the transceiver's SET mode. APPEAR allows scan type selection; 
   DISAPPEAR removes scan type selection from SET mode.

        Selectable value:    APPEAR or DISAPPEAR

        Selection method:    Push [Space] or [Backspace] to toggle the
                             selection.  



SCAN FUNCTION
   This item allows you to enable or disable the transceiver's scan functions.
   When this item is set to DISABLE, the SCAN MODE item (p. 5) is not
   available.

        Selectable value:    ENABLE or DISABLE

        Selection method:    Push [Space] or [Backspace] to toggle the
                             selection.       



WATCH MENU
   This item is used to add or remove watch type selection (dualwatch or
   tri-watch) from the transceiver's SET mode. APPEAR allows watch type
   selection; DISAPPEAR removes watch type selection from SET mode.

        Selectable value:    APPEAR or DISAPPEAR

        Selection method:    Push [Space] or [Backspace] to toggle the
                             selection.


















                                    - 6 -



////// MEMORY CHANNEL SCREEN //////

+[MEMORY CHANNEL]-----+-----+-----+-----+-----+
|CH  | CHANNEL  |LOCK-|Tx   |LOW  | DUP |SCRAM|
| No.|          |  OUT| INH | PWR |     |BLER |
+----+----------+-----+-----+-----+-----+-----+
|  0 | USA  16  |     |     |     |     |     |
|  1 | INHIBIT  |     |     |     |     |     |
|  2 | INHIBIT  |     |     |     |     |     |
~                                             ~  
~                                             ~  *                           *
| 23 | INHIBIT  |     |     |     |     |     |  * CH16 appears when "expert *
|CALL| USA  09  |  -  |     |     |     |     |  * is specified during       *
|CH16|      16  |  -  |     |     |     |  -  |  * program startup (p. 2)    *
+----+----------+-----+-----+-----+-----+-----+  *                           *  

This screen allows you to set all memory channel and call channel contents.


 SCREEN SELECTION

1) Push [Esc] key once or twice to indicate the TOP menu.

2) Select "Screen" with the [S] key, or the [Arrow] and [Enter] keys.
    - A sub menu appears under the TOP menu.


3) Select "Memory" with the [M] key, or the [Arrow] and [Enter] keys.
    - The MEMORY CHANNEL screen appears.



CHANNEL
The programmed channels appear when the MEMORY mode is selected.

1) Select the desired channel in the CHANNEL column with an [Arrow] key.

2) Push the [Space] or [Backspace] key to select the desired channel group:

      **  INT  16  **
      **  USA  16  **
      **  WX    1  **
      **  INHIBIT  **

3) Push digit keys to enter the desired marine channel number, 
   then push the [Enter] key. 
    - "A" can be input as a channel number.

4) Push [Enter] to enter the channel data.
    - The channel is highlighted and the [Arrow] and [Esc] keys can 
      be used. 











                                    - 7 -



LOCKOUT
The selected channels are locked out during memory scan. This setting can also 
be performed via the transceiver's front panel.

1) Select the desired channel in the LOCKOUT column with an [Arrow] key.

2) Push the [Space] key to select lockout or non-lockout.
    - "L" appears when lockout is specified and no indicator appears when
      lockout is canceled.



Tx INH
The selected channels can only receive; transmit is inhibited.

1) Select the desired channel in the Tx INH column with an [Arrow] key.

2) Push the [Space] key to select transmit inhibit or transmit non-inhibit.
   -"I" appears when transmit inhibit is specified and no indicator appears
    when transmit inhibit is canceled.



LOW POWER
The high/low power selection is disabled and only low power can be used on 
the selected channel.
 
1) Select the desired channel in the LOW PWR column with an [Arrow] key.

2) Push the [Space] key to select low or high power.
    - "P" appears when low power is specified and no indicator appears when
      high power is specified.

   **                                                                      **
   **  NOTE:  Low output power must be set when programming USA channels   **
   **         13 and 67.  The output power cannot be selected from the     **
   **         transceiver's front panel.                                   **
   **                                                                      **



DUP
Duplex information must be set for each channel (except when programming "A"
channels).  Otherwise, an incorrect frequency is transmitted. 

1) Select the desired channel in the DUP column with an [Arrow] key.

2) Push the [Space] key to select duplex or simplex.
    - "D" appears when duplex is specified and no indicator appears when
      simplex is specified.
    - "-" appears when "A" channels (e.g. channel 88A) are selected.
      In this case, a duplex setting cannot be specified.










                                    - 8 -



SCRAMBLER
  An optional UT-98 is required for the scrambler function. The scrambler
  function is turned ON for the selected channels. This setting can also be
  performed using the transceiver's front panel.

1) Select the desired channel in the SCRAMBLER column with an [Arrow] key.

2) Push the [Space] key to select scrambler function ON or OFF.
   -"S" appears when the scrambler function is turned ON.
   -No indication appears when the scrambler function is turned OFF.




















































                                    - 9 -



//////  INT CHANNEL and USA CHANNEL SCREENS  //////

+[INT CHANNEL]---+-----+------+-----++----+-----+-----+-----+------+-----+
|CH  |CH   |LOCK-|Tx   | LOW  | DUP ||CH  |CH   |LOCK-|Tx   | LOW  | DUP |
| No.| INH |  OUT| INH |  PWR |     || No.| INH |  OUT| INH |  PWR |     |
+----+-----+-----+-----+------+-----++----+-----+-----+-----+------+-----+
|  1 |     |     |     |      |  D  || 60 |     |     |     |      |  D  | 
|  1A|     |     |     |      |  -  || 60A|     |     |     |      |  -  | 
|  2 |     |     |     |      |  D  || 61 |     |     |     |      |  D  |
~                                                                        ~
~                                                                        ~
| 28A|  I  |     |     |      |  -  || 87A|     |     |     |      |  -  |
|    |  -  |  -  |  -  |  -   |  -  || 88 |     |     |     |      |  D  |
|    |  -  |  -  |  -  |  -   |  -  || 88A|     |     |     |      |  -  |
+----+-----+-----+-----+------+-----++----+-----+-----+-----+------+-----+


+[USA CHANNEL]---+-----+------+-----++----+-----+-----+-----+------+-----+
|CH  |CH   |LOCK-|Tx   | LOW  | DUP ||CH  |CH   |LOCK-|Tx   | LOW  | DUP |
| No.| INH |  OUT| INH |  PWR |     || No.| INH |  OUT| INH |  PWR |     |
+----+-----+-----+-----+------+-----++----+-----+-----+-----+------+-----+
|  1 |  I  |     |     |      |  D  || 60 |  I  |     |     |      |  D  | 
|  1A|     |     |     |      |  -  || 60A|     |     |     |      |  -  | 
|  2 |  I  |     |     |      |  D  || 61 |  I  |     |     |      |  D  |
~                                                                        ~
~                                                                        ~
| 28A|  I  |     |     |      |  -  || 87A|  I  |     |     |      |  -  |
|    |  -  |  -  |  -  |  -   |  -  || 88 |     |     |     |      |  D  |
|    |  -  |  -  |  -  |  -   |  -  || 88A|     |     |     |      |  -  |
+----+-----+-----+-----+------+-----++----+-----+-----+-----+------+-----+


When the international or USA channel group is selected with the transceiver, 
the channels in the screen table can be used.  When "I" (Inhibit) is selected
in the "CH INH" column, the selected channels do not appear in the selected
channel group. 



SCREEN SELECTION

1) Push [Esc] key once or twice to indicate the TOP menu.

2) Select "Screen" with the [S] key, or the [Arrow] and [Enter] keys.
    - A sub menu appears under the TOP menu.

3) Select "INT  ch" or "USA  ch" with the [I] or [U] key, or the [Arrow] 
   and [Enter] keys.
    - The INT CHANNEL or USA CHANNEL screen appears.



CH INH
The selected channels do not appear during channel selection.

1) Select the desired channel in the CH INH column with an [Arrow] key.

2) Push the [Space] key to toggle the "I" or no indication selection.
    - "I" means inhibit. 
    - No indication means the channel appears and can be used during 
      operation.

                                    - 10 -



LOCKOUT
The selected channel is locked out during scan. This setting can also be 
performed using the transceiver's front panel.

1) Select the desired channel in the LOCKOUT column with an [Arrow] key.

2) Push the [Space] key to select lockout or non-lockout.
    - "L" appears when lockout is specified and no indicator appears when
      lockout is canceled.



Tx INH
The selected channel can receive only; transmit is inhibited.

1) Select the desired channel in the Tx INH column with an [Arrow] key.

2) Push the [Space] key to select transmit inhibit or transmit non-inhibit.
   - "I" appears when transmit inhibit is specified and no indicator appears
     when transmit inhibit is canceled.



LOW POWER
The high/low power selection is disabled and only low power can be used on 
the selected channel.
 
1) Select the desired channel in the LOW PWR column with an [Arrow] key.

2) Push the [Space] key to select low or high power.
    - "P" appears when low power is specified and no indicator appears when
      high power is specified.

  **                                                                      **
  **                                                                      **
  **  NOTE:  Low output power must be set on USA channels 13 and 67.      **
  **         The output power cannot be selected from the transceiver's   **
  **         front panel.                                                 **
  **                                                                      **



DUP
Duplex information must be set for each channel (except when programming "A"
channels).  Otherwise, an incorrect frequency is transmitted. 

1) Select the desired channel in the DUP column with an [Arrow] key.

2) Push the [Space] key to select duplex or simplex.
    - "D" appears when duplex is specified and no indicator appears when
      simplex is specified.
    - "-" appears when "A" channels (e.g. channel 88A) are selected.
      In this case, a duplex setting cannot be specified.









                                    - 11 -



////// PRIVATE CHANNEL SCREENS //////

+[INT PRIVATE CHANNEL]-+-----+-----++----+-----+-----+-----+-----+-----+
|CH  |CH   |LOCK-|Tx   |LOW  | DUP ||CH  |CH   |LOCK-|Tx   |LOW  | DUP |
| No.| INH |  OUT| INH | PWR |     || No.| INH |  OUT| INH | PWR |     |
+----+-----+-----+-----+-----+-----++----+-----+-----+-----+-----+-----+
| 29 |  I  |     |     |     |  D  || 89 |  I  |     |     |     |  D  | 
| 29A|  I  |     |     |     |  -  || 89A|  I  |     |     |     |  -  | 
| 30 |  I  |     |     |     |  D  || 90 |  I  |     |     |     |  D  |
~                                                                      ~
~                                                                      ~
| 58A|  I  |     |     |     |  -  ||  0A|  I  |     |     |     |  -  |
| 59 |  I  |     |     |     |  D  ||    |  -  |  -  |  -  |  -  |  -  |
| 59A|  I  |     |     |     |  -  ||    |  -  |  -  |  -  |  -  |  -  |
+----+-----+-----+-----+-----+-----++----+-----+-----+-----+-----+-----+



+[USA PRIVATE CHANNEL]-+-----+-----++----+-----+-----+-----+-----+-----+
|CH  |CH   |LOCK-|Tx   |LOW  | DUP ||CH  |CH   |LOCK-|Tx   |LOW  | DUP |
| No.| INH |  OUT| INH | PWR |     || No.| INH |  OUT| INH | PWR |     |
+----+-----+-----+-----+-----+-----++----+-----+-----+-----+-----+-----+
| 29 |  I  |     |     |     |  D  || 89 |  I  |     |     |     |  D  |
| 29A|  I  |     |     |     |  -  || 89A|  I  |     |     |     |  -  |
| 30 |  I  |     |     |     |  D  || 90 |  I  |     |     |     |  D  |
~                                                                      ~
~                                                                      ~
| 58A|  I  |     |     |     |  -  ||  0A|  I  |     |     |     |  -  |
| 59 |  I  |     |     |     |  D  ||    |  -  |  -  |  -  |  -  |  -  |
| 59A|  I  |     |     |     |  -  ||    |  -  |  -  |  -  |  -  |  -  |
+----+-----+-----+-----+-----+-----++----+-----+-----+-----+-----+-----+


The transceiver has preset private channels.  When "I" (Inhibit) is cleared
in the "CH INH" column, the selected channels appear in the international or
USA channel group.



SCREEN SELECTION

1) Push [Esc] key once or twice to indicate the TOP menu.

2) Select "Screen" with the [S] key, or an [Arrow] and [Enter] keys.
    - A SUB menu appears under the TOP menu.

3) Select the desired channel screen:
    - For INT (PRV)ch screen, push [N], or the [Arrow] and [Enter] keys.
    - For USA (PRV)ch screen, push [S], or the [Arrow] and [Enter] keys.



CH INH
The selected channels ("I" is indicated) do not appear during channel 
selection.

1) Select the desired channel in the CH INH column with an [Arrow] key.

2) Push the [Space] key to toggle the "I" or no indication selection.
    - "I" means Inhibit. 
    - No indication means the channel appears and can be used 
      during operation.
                                    - 12 -



LOCKOUT
The selected channel is locked out during scan. This setting can also be 
performed using the transceiver's front panel. 

1) Select the desired channel in the LOCKOUT column with an [Arrow] key.

2) Push the [Space] key to select lockout or non-lockout.
    - "L" appears when lockout is specified and no indicator appears when
      lockout is canceled.



Tx INH
The selected channel can receive only; transmit is inhibited.

1) Select the desired channel in the Tx INH column with an [Arrow] key.

2) Push the [Space] key to select transmit inhibit or transmit non-inhibit.
   - "I" appears when transmit inhibit is specified and no indicator appears
     when transmit inhibit is canceled.



LOW POWER
The high/low power selection is disabled and only low power can be used on 
the selected channel.

1) Select the desired channel in the LOW PWR column with an [Arrow] key.

2) Push the [Space] key to select low or high power.
    - "P" appears when low power is specified and no indicator appears when
      high power is specified.



DUP  
Duplex information must be set for each channel (except when programming "A"
channels).  Otherwise, an incorrect frequency is transmitted. 

1) Select the desired channel in the DUP column with an [Arrow] key.

2) Push the [Space] key to select duplex or simplex.
    - "D" appears when duplex is specified and no indicator appears when
      simplex is specified.
    - "-" appears when "A" channels (e.g. channel 88A) are selected.
      In this case, a duplex setting cannot be specified.
















                                    - 13 -



////// FREE CHANNEL SCREEN //////

+[FREE CHANNEL]--+-----+-----+-----------+-----------+
|CH  |CH   |LOCK-|Tx   |LOW  | RX FREQ.  |  TX FREQ. |
| No.| INH |  OUT| INH | PWR |    [MHz]  |     [MHz] |
+----+-----+-----+-----+-----+-----------+-----------+
| F1 |  I  |     |     |     | --------- | --------  |
| F2 |  I  |     |     |     | --------- | --------  |
| F3 |  I  |     |     |     | --------- | --------  |
~                                                    ~
~                                                    ~
| P7 |  I  |     |     |     | 156.80000 | 156.80000 |
| P8 |  I  |     |     |     | 156.80000 | 156.80000 |
| P9 |  I  |     |     |     | 156.80000 | 156.80000 |
+----+-----+-----+-----+-----+-----------+-----------+

The transceiver has preset and programmable free channels. Channels F1 to F7,
L1 to L3, C1 to C4, E1 and P1 to P3 are preset (receive and transmit
frequencies cannot be programmed). Channels P4 to P9 can be programmed with
receive and transmit frequencies. 


SCREEN SELECTION

1) Push [Esc] key once or twice to indicate the TOP menu.

2) Select "Screen" with the [S] key, or the [Arrow] and [Enter] keys.
    - A SUB menu appears under the TOP menu.

3) Select "FREE ch" with the [F] key, or the [Arrow] and [Enter] keys.



CH INH
The selected channels ("I" is indicated) do not appear during channel
selection.

1) Select the desired channel in the CH INH column with an [Arrow] key.

2) Push the [Space] key to toggle the "I" or no indication selection.
    - "I" means Inhibit. 
    - No indication means the channel appears and can be used 
      during operation.



LOCKOUT
The selected channel is locked out during scan. This setting can also be
performed using the transceiver's front panel.

1) Select the desired channel in the LOCKOUT column with an [Arrow] key.

2) Push the [Space] key to select lockout or non-lockout.
    - "L" appears when lockout is specified and no indicator appears when
      lockout is canceled.







                                    - 14 -



Tx INH
The selected channel can receive only; transmit is inhibited.

1) Select the desired channel in the Tx INH column with an [Arrow] key.

2) Push the [Space] key to select transmit inhibit or transmit non-inhibit.
   - "I" appears when transmit inhibit is specified and no indicator appears
     when transmit inhibit is canceled.



LOW POWER
The high/low power selection is disabled and only low power can be used on 
the selected channel.

1) Select the desired channel in the LOW PWR column with an [Arrow] key.

2) Push the [Space] key to select low or high power.
    - "P" appears when low power is specified and no indicator appears when
      high power is specified.



RX FREQ. [MHz]/TX FREQ. [MHz]
Receive and transmit frequencies can be set here (channels P4 to P9 only).

1) Select the desired channel in the RX FREQ. [MHz] or TX FREQ. [MHz] column
   with an [Arrow] key.

2) Push the digit keys, then push [Enter] to input a receive or transmit
   frequency.
   - 100.00000 to 199.9950 MHz can be input.

     **                                                              **
     ** NOTE: Even though out-of-range frequencies can be set, the   **
     **       transceiver may not accept such frequencies.           **
     **                                                              **

























                                    - 15 -



////// WX CHANNEL SCREEN //////

+[WX CHANNEL]----+
|CH  |CH   |LOCK-|
| No.| INH |  OUT|
+----+-----+-----+
|  1 |     |     |
|  2 |     |     |
|  3 |     |     |
|  4 |     |     |
|  5 |     |     |
|  6 |     |     |
|  7 |     |     |
|  8 |     |     |
|  9 |     |     |
| 10 |     |     |
+----+-----+-----+

When weather channels are selected with the transceiver, the channels in 
the screen table can be used.  When "I" (Inhibit) is selected in the "CH INH"
column, the selected channels do not appear in the selected channel group. 



SCREEN SELECTION

1) Push [Esc] key once or twice to indicate the TOP menu.

2) Select "Screen" with the [S] key, or the [Arrow] and [Enter] keys.
    - A SUB menu appears under the TOP menu.

3) Select "WX   ch" with the [W] key, or the [Arrow] and [Enter] keys.
    - The WX CHANNEL screen appears.



CH INH
The selected channels do not appear during channel selection.

1) Select the desired channel in the CH INH column with an [Arrow] key.

2) Push the [Space] key to toggle the "I" or no indication selection.
    - "I" means inhibit. 
    - No indication means the channel appears and can be used during 
      operation.



LOCKOUT
The selected channels are locked out during scan. This setting can also be
performed via the transceiver's front panel.

1) Select the desired channel in the LOCKOUT column with an [Arrow] key.

2) Push the [Space] key to select lockout or non-lockout.
    - "L" appears when lockout is specified and no indicator appears when
      lockout is canceled.





                                    - 16 -



-------------------------------------------------------------------------------
4. CLONING OPERATION
-------------------------------------------------------------------------------

Programmed data can be cloned to an IC-M10A/E instantly.  All data is clone
sent from PC to transceiver (PC -> TR) or clone read from transceiver to PC
(PC <- TR) for approx. 15 sec.  A cloning cable, the OPC-478, is needed to
connect a PC's RS-232C port to the transceiver. 

For convenience, when changing a small portion of the programmed contents, 
clone read the data from the transceiver, modify the data, then clone send 
it back to the transceiver. 



CLONE SEND
The programmed data in the PC is copied to the transceiver.

1) Connect the OPC-478 with supplied asapter plug (MA-235SPJ) between the PC's 
   RS-232C terminal and transceiver's [MIC] jack.

2) Turn the PC and transceiver power ON.

3) Start up this program.

4) Select "Clone" in the TOP menu with the [C] key, or the [Arrow] and 
   [Enter] keys.
     - Clone sub menu appears.

5) Select "PC -> TR" in the SUB menu with the [P] key, or the [Arrow] and 
   [Enter] keys.
     - "Sending oooooo" appears in the bottom left of corner of the screen.
     - "CL" and "BUSY" appear on the transceiver display.
     - When cloning is finished, "BUSY" disappears.

          **                                                        **
          **  NOTE: When the wrong port is selected on the RS-232C  **
          **        port, "ERROR: CLONE error" appears in the       **
          **        bottom left corner of the screen.  In this      **
          **        case, check the selection as described on the   **
          **        following page. Also, operating the transceiver,**
          **        such as rotating the transceiver's channel      **
          **        selector knob just before hitting the [Enter]   **
          **        key may result in a cloning error.              **
          **                                                        **

6) Turn the transceiver OFF and ON again.
     - Clone send is now complete.














                                    - 17 - 



CLONE READ
The pre-set data in the transceiver is copied to the PC.

1) Connect the OPC-478 with supplied adapter plug (MA-235SPJ) between the PC's 
   RS-232C terminal and transceiver's [MIC] jack.

2) Turn the PC and transceiver power ON.

3) Start up this program.

4) Select "Clone" in the TOP menu with the [C] key, or the [Arrow] and 
   [Enter] keys.
     - Clone sub menu appears.

5) Select "PC <- TR" in the sub menu with the [T] key, or the [Arrow] and 
   [Enter] keys.
     - "CL" and "BUSY" appear on the transceiver's display.
     - When cloning is finished, the transceiver's display returns to 
       previous indication.
     - When cloning is finished, "BUSY" disappears.
     - Turn the transceiver OFF and ON to return to the previous display.



RS-232C
When the connected PC has 2 or more RS-232C ports, the desired port can be 
selected with this program.  When the PC has only 1 port, "PORT #1" must be
selected, otherwise, the cloning operation cannot be performed.


1) Select "Clone" in the TOP menu with the [C] key, or an [Arrow] and 
   [Enter] keys.
    - Clone sub menu appears.

2) Select "RS-232C" in the SUB menu with the [R] key, or the  [Arrow] and
   [Enter] keys.
    - RS-232C port selection block appears.

3) Select the desired port number to connect the cloning cable with the 
   [Arrow] and [Enter] keys.
    - Selected number is the same as the PC port number assignment.





















                                    - 18 -



-------------------------------------------------------------------------------
5. FILE SAVING AND LOADING 
-------------------------------------------------------------------------------

PROGRAM INFORMATION
The EX-1700 contains the following:

       EX1700.EXE    : Main program
       M10EUR.INI    : Europe version default settings
       M10UK.INI     : UK version default settings
       M10USA.INI    : USA version default settings
       M10HOL.INI    : Holland version default settings
       M10FRA.INI    : France version default settings
       M10.DOC       : This document file

When starting up this program and no version name, such as USA, EUR, UK, HOL 
or FRA is used, or an invalid version name is used, USA.INI is loaded.



FILE SAVING OPERATION

1) Push [Esc] to indicate the TOP menu.

2) Select "File" in the TOP menu with the [F] key, or the [Arrow] and 
   [Enter] keys.
     - File sub menu appears.

3) Select "Save" in the sub menu with the [S] key, or [Arrow] and 
   [Enter] keys.
     - A file name box appears and shows "FILE: noname.icf". 

4) Type the desired file name to be saved.
     - ICF is recommended as a file extension for loading convenience.
     - When no file extension is used, ".ICF" is automatically added to the 
       file name.
     - The TOP menu and the file name disappear and the previous menu appears.

**                                                                        **
**  SAVING NOTE:                                                          **
**                                                                        **
**  An initial setting file name such as "M10USA.INI" cannot be used      ** 
**  as a saved file name, since overwriting the initial setting is        **
**  inhibited.                                                            **
**                                                                        **
**  When starting up the program and no file name has been loaded,        **
**  "noname.icf" appears in the file name box.  In this case, direct      **
**  file name entry is possible ("noname" disappears automatically).      **
**  However, once a file is loaded or saved, file name entry does not     **
**  change the file name. ([Del] or [Ins] key must be used to change the  **
**  file name.)                                                           **
**                                                                        **
**  To indicate the previously saved file name, "*" (wild card) may be    **
**  helpful to check the file name.                                       **
**                                                                        **







                                    - 19 -



FILE LOADING OPERATION

1) Push [Esc] to indicate the TOP menu.

2) Select "File" in the TOP menu with the [F] key, or the [Arrow] and 
   [Enter] keys.
     - File sub menu appears.

3) Select "Load" in the SUB menu with the [L] key, or [Arrow] and 
   [Enter] keys.
    - A file name box appears and shows "FILE: *.ICF".

4) Type the desired file name, then push [Enter].
   Or, push [Enter] to indicate the pre-programmed file name, select the
   desired file name with an [Arrow] key, then push the [Enter] key twice. 
    - The typed or selected file is loaded, then the file name box 
      disappears.
    - The loaded file name appears in the bottom left corner of the screen.




DOS COMMAND
 In the "File" sub menu, a "Dos" item appears.  This command pauses the
 program so that a DOS command can be used.  When you want to return to 
 normal operation of the program, type "EXIT", then push [Enter].




































                                    - 20 -



-------------------------------------------------------------------------------
6. PRINTING
-------------------------------------------------------------------------------

The set data can be printed out for convenience and reference for subsequent
programming.  Only the currently displayed screen is printed out, therefore, 
the printout operation must be performed for each screen desired. 


1) Push [Esc] to indicate the TOP menu.

2) Select "Print" in the TOP menu with the [P] key, or the [Arrow] and 
   [Enter] keys.
     - Print sub menu appears and shows "Current".

3) Push [Enter] again to print out the currently displayed data.
       
4) After printing is complete, the TOP and SUB menus disappear.












































                                    - 21 -